Steca Elektronik GmbH | 87700 Memmingen | Germany | Fon +49 (0) 8331 8558-0 | Fax +49 (0) 8331 8558-132 | www.steca.com

Steca Solarix

2401, 4401

The solar charge controllers Steca Solarix 2401 and 4401 are optimally suited for inverter systems. The controller combines basic solar charger functions with a 40 A high-performance charge controller. It is available as 1 2 V / 24 V and 48 V system. This makes the solar charge controller very cost effective.

The load current is limited to 10 A. The charging processes are based on the voltage level, which can be individually set with the help of four buttons behind the front casing.

Product features

- [40 A

m

■	Hybrid controller

■	Voltage regulation

■	Automatic detection of voltage

■	PWM contro

■	Multistage charging technology

■	Load disconnection depending on voltage

■	Automatic load reconnection

■	Temperature compensation

■	Common positive grounding or negative grounding on one termina

■	Integrated self test

■	Monthly maintenance charge

Electronic protection functions

|  | 2401 4401 |
| --- | --- |
|  | Characterisation of the operating performance |
|  | System voltage | 12 V (24 V) 48 V |
|  | Own consumption | 14 mA |
|  | DC input side |
|  | Module current 40 A |
|  | DC output side |
|  | Load current | 10 A |
|  | End of charge voltage | 13.7 V (27.4 V) | 54.8 V |
|  | Boost charge voltage | 14.4 V (28.8 V) | 57.6 V |
|  | Equalisation charge | 14.7 V (29.4 V) | 58.8 V |
|  | Reconnection voltage (LVR) | 12.6 V (25.2 V) | 50.4 V |
|  | Deep discharge protection (LVD) | 11.1 V (22.2 V) | 44.4 V |
|  | Operating conditions |
|  | Ambient temperature -10 °C … +60 °C |
|  | Fitting and construction |
|  | Terminal (fine / single wire) | 16 mm2 / 25 mm2 - AWG 6 / 4 |
|  | Degree of protection | IP 32 |
|  | Dimensions (X x Y x Z) | 187 x 128 x 49 mm |
|  | Weight | 550 g |

■	Overcharge protection

■	Deep discharge protection

■	Reverse polarity protection of load, module and battery

■	Reverse polarity protection by internal fuse

■	Automatic electronic fuse

■	Short circuit protection of load and module

■	Overvoltage protection at module input

■	Open circuit protection without battery

■	Reverse current protection at night

■	Overtemperature and overload protection

■	Battery overvoltage shutdown

Displays

■	Text LCD display

— for operating parameters, fault messages, self test

Operation

■	Simple menu-driven operation

■	Programming by buttons

■	Manual load switch

Technical data at 25 °C / 77 °F

Interfaces

■	RJ45 interface

Steca PA TSK10

External temperature sensor

Options

■	External temperature sensor

■	Alarm contact

Certificates

■	Compliant with European Standards (CE)

■	Made in Germany

■	Developed in Germany

■	Manufactured according to ISO 9001 and ISO 14001

■[areas of application]